## Slide 1
DCVC-RT 容错：latent 分层传输与渐进质量退化
基于 3GPP SA4#137-e S4-261527/261528：neural video/image codec 作为 LLM/MLLM intermediate data 的传输对象
FS_6G_MED / TR 26.870
1. DCVC-RT Intermediate Data
2. Fault-Tolerance Evidence
3. Transport Design Implications
Why DCVC-RT is relevant
Representative neural codec for intermediate data transfer to LLM/MLLM workflows.
Reported as ~21% bitrate saving vs H.266/VTM for 1080p video; ~385 GMAC/frame enables 1080p30 on recent mobile SoCs.
Produces continuous intermediate data: hyper-latent Zt plus main-latent slices y0..y3, decoded cumulatively.
Dependency graph
Zt is mandatory side information for reconstruction.
y0..y3 refine quality progressively; each later slice depends on successful availability of earlier slices.
Loss of yn prevents yn+1, yn+2... from contributing to quality improvement.
Zt
y0
y1
y2
y3
容错不是均匀保护问题，而是有强优先级和顺序依赖的 layered protection 问题。
Reconstruction set | Data | PSNR | Interpretation
Zt only | 3.1% | 21.45 dB | coarse base
Zt+y0 | 32.1% | 25.82 dB | major gain
Zt+y0+y1 | 56.6% | 28.93 dB | near 30 dB
Zt+y0+y1+y2 | 79.1% | 32.61 dB | passes 30 dB
all | 100% | 39.83 dB | full quality
Experiment 1: progressive add-back
Dropping main latent and adding y0..y3 back shows monotonic quality refinement.
A 30 dB operating point may be reached before all latent slices are delivered, depending on content complexity.
Loss case | Remaining data | PSNR / result | Fault impact
drop Zt | 89.8% | 9.67 dB | cannot reconstruct
Zt only | 10.3% | 27.79 dB | base image
Zt+y0 | 38.9% | 32.74 dB | 30 dB target ok
Zt+y0+y1 | 62.1% | 36.19 dB | enhanced
all | 100% | 44.70 dB | reference
Experiment 2: intentional latent loss
Zt loss is catastrophic even with most bytes present; later y-slice loss causes graceful but content-dependent degradation.
Unequal error protection
Protect Zt with strongest reliability: duplication, HARQ priority, FEC, or lower PER QoS flow.
Protect y0 next; later y slices can tolerate higher loss if application accepts lower reconstruction quality.
Progressive delivery policy
Transmit base dependency chain first: Zt -> y0 -> y1 -> y2 -> y3.
Allow early decode or partial decode once use-case PSNR/MLLM utility target is met.
Packetization semantics
Network packets should expose latent slice identity and dependency order to enable selective retransmission/prioritization.
A missing earlier slice wastes transmission of dependent later slices unless decoder has explicit recovery logic.
Standardization questions
Study exact role/count of latent components: decode-pipelining vs progressive-quality refinement.
Define graceful degradation metrics beyond PSNR, including downstream LLM/MLLM task accuracy.
Technical takeaway
DCVC-RT intermediate data has a non-uniform value structure: a small hyper-latent can dominate decodability, while main-latent slices provide scalable refinement.
容错策略应从 byte-level 均匀保护转为 dependency-aware protection：Zt catastrophic loss, y-slice graceful degradation, later slices conditional on earlier delivery.
For 6G-MED, the useful abstraction is a layered AI representation stream with per-layer importance, dependency metadata, and content/use-case-specific minimum quality thresholds.
Sources: 3GPP SA4#137-e S4-261527.zip and S4-261528.zip | DCVC-RT progressive reconstruction experiments and TR 26.870 pCR text