## Slide 1
Agentic AI 流量特性分析：本地 Agent 与 A2A 协作
基于 3GPP SA4#137-e S4-261814：OpenClaw personal assistant + Agent2Agent deterministic collaboration across 10 network profiles
S4-261814 / TR 26.870 pCR
1. Measurement Scope
2. Quantified Traffic Surfaces
3. Network Design Implications
Personal assistant agent
Local-first OpenClaw runtime on UE/user device; runtime invokes commercial/local LLM plus browser/file/shell tools.
Two surfaces measured separately: loopback control channel and WAN runtime egress to LLM/tools.
Fresh session per task avoids monotonically increasing history/context across runs.
Agent-to-Agent collaboration
A2A protocol: AgentCard capability discovery, message/send non-streaming, message/stream over SSE.
Deterministic agents without LLM isolate protocol + transport cost from inference variance.
Three modes: single task, streaming delegation, multi-agent sequential fan-out to two peers.
Scenario | Turns | Profiles | Success | Mean lat.
OpenClaw PA | 200 | 10 | 100% | 14.694 s
A2A single | 198 | 10 | 98.5% | 0.174 s
A2A stream | 99 | 10 | 100% | 0.435 s
A2A multi | 100 | 10 | 99.0% | 0.547 s
Prompt
Context + Tools
LLM/Tool Calls
Agent turn 的网络视角是 repeated context upload + tool fan-out，不等同于一次普通 chat API call。
Layer mismatch: app-layer 与 network-layer 结论相反
Control-channel driver view: 144 B UL / 20,230 B DL，UL/DL = 0.007，表面上极度 DL-heavy。
WAN runtime egress: 175,649 B UL / 353,972 B DL，UL/DL = 0.496，接入网实际承载近似对称。
原因：每个 agent step 重传 accumulated context、system prompt、tool definitions。
Surface | UL/turn | DL/turn | UL/DL | Layer
PA control | 3.8 KB | 50.0 KB | 0.076 | net
PA WAN | 175.6 KB | 354.0 KB | 0.496 | net
A2A loopback | 1.9 KB | 4.1 KB | 0.473 | net
A2A stream app | 565 B | 202 B | 2.797 | app
Latency decomposition
Personal assistant: inference + tool execution dominates; no_emulation 11.4 s, congested 26.6 s, satellite_geo 24.4 s.
A2A deterministic path: latency tracks RTT; single task 0.002 s baseline -> 0.687 s GEO.
Streaming adds inter-chunk spacing; multi-agent adds ~0.28 s fixed orchestration cost.
Profile | PA | A2A single | A2A stream | A2A multi
no emu. | 11.415 | 0.002 | 0.205 | 0.277
cell-edge | 18.074 | 0.321 | 0.558 | 0.940
sat GEO | 24.356 | 0.687 | 0.902 | 0.960
congested | 26.587 | 0.434 | 1.161 | 1.324
Uplink grant latency gates agentic workloads
Agentic traffic breaks classical media DL-heavy capacity assumption.
Repeated context/tool definition upload makes UL scheduling and buffer sizing visible at service latency level.
Small signaling, high sensitivity to PER
A2A messages are only a few hundred bytes at application layer, so bandwidth is not limiting.
Delay alone is tolerated, but lossy profiles caused the observed A2A failures; target low PER over high throughput.
Connection behavior matters as much as payload
OpenClaw egress: 2.46 TCP flows/turn, 28 distinct destinations, TLS handshake p50 1.33 s / p95 3.64 s.
0-RTT resumption, connection coalescing and persistent multiplexed transports can beat raw capacity upgrades.
Recommended traffic model axes
Model by surface: local control, WAN runtime egress, A2A interworking.
Metrics: UL/DL per turn, flow fan-out, setup/TLS time, retransmission rate, agent steps/tool calls, RTT/loss sensitivity.
Technical Takeaway
Agentic AI should be dimensioned as a compound control/signaling workload: many encrypted short flows, repeated state upload, and tool/API fan-out.
Personal assistant traffic is inference-variance dominated until severe impairment; A2A traffic is RTT/PER dominated because deterministic agents remove model compute from the path.
For 6G AI/ML service traffic models, network-layer measurements are mandatory: application payload alone can misclassify the directionality by two orders of magnitude.
Source: 3GPP SA4#137-e S4-261814.zip, Collated_AI_Traffic_Results_note_0_5_1_A2A.xlsx | Metrics from packet captures exclude bookkeeping records