## Slide 1
AI-native Representation Transport：Tokenized Traffic 的传输与信令问题
基于 3GPP SA4#137-e S4-261805：tokens / embeddings / latents / feature tensors 从模型内部表示变成 6G media 通信对象
TR 26.870 v0.5.1 pCR
1. Representation Is The Payload
2. Transport & Signalling Gap
3. Study Questions For 6G-MED
Tokenized traffic vs representation transport
Tokenized traffic: token counts/rates, inter-token gaps, TTFT/TTLT and burstiness measured from logs, traces or PCAP.
AI-native representation transport: explicit carriage of model-consumable units such as discrete tokens, embeddings, latents and tensors.
The second case raises media-layer questions that ordinary traffic metrics do not answer.
Why this matters for traffic characteristics
UE may transmit task-relevant representations instead of full camera/microphone/sensor media.
Conventional media and AI-native representations may be sent together: one stream for human consumption, one for AI processing.
Task-oriented compression shifts optimization target from signal reconstruction to downstream inference/control utility.
Representation | Typical source | Traffic implication
Visual token | VLM/video tokenizer | periodic or bursty token stream
Embedding | image/audio/sensor encoder | metadata-bound vector payload
Latent | generative model codec | compressed semantic state
Feature tensor | machine analysis pipeline | shape/model-dependent payload
Source media
Tokenizer/ Encoder
AI-native representation
Inference / AI media fn
Current TR gap
TR 26.870 has initial traffic characterization metrics, but not transport/signalling for delay-bound representation streams.
Open questions include packetization, fragmentation, aggregation, timing, stream association, synchronization and receiver interpretation.
Metadata is needed to identify representation type, model/encoder, source media correlation and processing semantics.
RTP/SDP is a candidate, but not sufficient yet
RTP already supports time-sensitive packetized media and WebRTC/3GPP real-time sessions.
SDP can negotiate payload formats and media parameters.
No interoperable RTP payload format or SDP signalling model is identified for AI-native representation streams.
Layer | Required study item | Why
Payload | format, shape, quantization | receiver/model compatibility
Packet | fragment/aggregate policy | MTU, loss, latency
Session | SDP capability negotiation | interoperability
Timing | RTP timestamp / sync | align with source media
Metadata | encoder/model/source id | semantic interpretation
Key issue 1: representation taxonomy
Identify relevant AI-native formats for 6G media: discrete tokens, continuous embeddings, latents, feature tensors and other intermediate AI data.
Classify whether they are media-derived, model-derived, task-derived, or network-assisted processing artifacts.
Key issue 2: traffic and QoS requirements
For each UE-network-server-peer exchange, define latency, reliability, synchronization and traffic characteristic requirements.
Token-level reliability can be unequal: semantically important units may need differentiated protection.
Key issue 3: media association
Representations may be derived from video/audio/sensor streams and consumed alongside original media.
Study stream grouping, timestamp mapping, source correlation and cross-modal synchronization.
Key issue 4: protocol extension scope
Assess whether existing media transport/signalling is enough.
Potential extensions: RTP payload formats, SDP parameters, grouping semantics, metadata schemas and receiver capability signalling.
Technical takeaway
S4-261805 moves the discussion from measuring token-related app behaviour to transporting AI-native representation streams as first-class media objects.
For 6G-MED, the critical modelling unit is no longer only bytes or tokens per second; it is representation units with timing, model identity, source-media binding and task-level importance.
The proposed TR 26.870 work should connect traffic characterization with interoperable transport/signalling design: packetization, RTP/SDP or alternatives, metadata, synchronization and QoS semantics.
Source: 3GPP SA4#137-e S4-261805.zip, S4-261805_26870_[FS_6G_MED]_pCR_tokenized_traffic.docx | Nokia | revision of S4-261450