## Slide 1
多模态意图理解：6G Media Service 侧的语义抽象与边界
基于 3GPP SA4#137-e S4-261484 / S4-261648：将 gaze、gesture、speech、scene、text、device context 转换为 media-service intent
FS_6G_MED WT2
1. Intent Understanding Pipeline
2. SA4 Scope And Interfaces
3. Study Issues For TR 26.870
Input signal space
Multimodal context: audio, video, haptics, scene description, gaze, gestures, text, device context.
Sensitive by default: speech content, first-person video, accessibility context and personal preferences.
Raw signal exposure should not be the default network interface.
Signals
Fusion/ Inference
Intent Abstraction
Media Action
Media intent | Observable context | Service behaviour
Focus speaker | gaze + speech + scene | view/crop/audio focus
Preserve haptics | gesture + haptic state | latency/QoE priority
Switch viewpoint | pose + text command | camera/viewport change
Adapt avatar | video + preference | representation selection
Technical abstraction
Intent is not a NAS/network command; it is media-service-level interpretation of user/application objective.
Output should be structured media requirements or adaptation requests, not unconstrained user-context dumps.
Boundary with SA2 intent work
SA2 studies 6G system architecture intent handling, including network-level intent and request fulfilment.
SA4 should study media-service intent: session control, media processing, adaptation and QoE support.
Avoid duplicating NAS intent transport or system-level intent orchestration.
Function placement
Do not assume UE MT stack produces/parses media intents.
Intent understanding may run in media-service functions according to delivery architecture.
WT2 asks which AI/ML functions run on-device vs network, and what formats/protocols cross the interface.
Layer | In SA4 scope | Out / coordinate
Media app | objective inference | raw privacy leakage
Session | media adaptation/control | NAS intent transport
QoE | haptic, viewpoint, avatar needs | network intent fulfilment
Format | media AI data components | SA2 architecture semantics
pCR insertion point
S4-261648 proposes updating TR 26.870 clause 6.3.4 AI services and formats to include service models/formats for media services involving multimodal user intents.
Terminology and representation
Define intent object semantics: user objective, application objective, confidence, time validity, source modality references.
Represent intent as media-service requirements where possible.
Formats and protocols
Identify exchanged formats between UE and network/media-service functions.
Study whether intent metadata belongs in media session signalling, application API payloads, or AI-native representation descriptors.
Privacy-preserving exposure
Minimize context crossing network interfaces; expose only authorized, structured and purpose-limited data.
Prefer derived intent/requirement over gaze video, raw speech, preference history, or accessibility context.
Traffic and QoE characterization
Intent understanding impacts traffic through adaptation decisions rather than only adding payload bytes.
Metrics should link inference latency, confidence, modality freshness and QoE outcome.
Technical takeaway
多模态意图理解应定义为 media-service semantics：用多模态上下文推断用户/应用目标，并驱动媒体处理、会话控制、适配和 QoE 支持。
SA4 的关键不是复刻 SA2 network-level intent，而是定义媒体服务可消费的 intent abstraction、函数部署位置、数据格式、协议边界和隐私最小化原则。
在 TR 26.870 中，intent 可作为连接 AI service models/formats 与 traffic/QoE characterization 的控制面抽象：影响媒体流选择、优先级、同步和表示方式。
Sources: 3GPP SA4#137-e S4-261484.zip and S4-261648.zip | InterDigital Canada | FS_6G_MED WT2 / TR 26.870 clause 6.3.4